## Slide 1
Process Safety Management
Of Highly Hazardous Chemicals

## Slide 2: What is Process Safety Management?
In 1992, OSHA developed the Process Safety Management rule,
29 CFR 1910.119 due to many industrial incidents
Involving highly hazardous chemical releases.
The intent of this rule is to prevent or minimize the consequences
of catastrophic releases of toxic, reactive, flammable, or
explosive chemicals.
The chemical of concern present at the Rumford mill is the
manufacturing of chlorine dioxide (ClO2).
Notes: Personal safety accountability. Always look out for one another – the primary goal is to go home how we came in.

## Slide 3: What is Chlorine Dioxide – ClO2?
Chlorine dioxide (ClO2) is a chemical used in the pulp and
paper industry to bleach pulp for white paper products.
Because the gas is unstable, it cannot be transported and is
always produced where the bleaching occurs.
The ClO2 is manufactured at the Rumford Mill in the R8 Plant
building.
Notes: Personal safety accountability. Always look out for one another – the primary goal is to go home how we came in.

## Slide 4: What is Chlorine Dioxide – ClO2?
ClO2 is a yellowish-green gas that is converted into an
aqueous solution. ClO2 smells of bleach and can be detected
very quickly.
When there is exposure to ClO2, this can cause respiratory
Irritation and ingestion can be harmful.
Always report to a ND paper representative if you suspect there
May be ClO2 gas present in the area you are working.
Fixed monitors are throughout the R8 building to detect ClO2. In
the event of alarms going off, immediately exit the building.
Notes: Personal safety accountability. Always look out for one another – the primary goal is to go home how we came in.

## Slide 5: 14 Elements of Process Safety Management
The following are the elements which make up the process
safety management program:
Employee Participation Process Safety Information
Process Hazard Analysis Operating Procedures
Employee Training Contractors
Management of Change Prestart up Safety Review
Mechanical Integrity Hot Work
Incident Investigation Emergency Planning & Response
Compliance Audits Trade Secrets
Notes: Personal safety accountability. Always look out for one another – the primary goal is to go home how we came in.

## Slide 6: Employer responsibilities for contractors
The employer responsibilities for contractors work on or near a
PSM-covered process:
The employer must obtain and evaluate information regarding the
contractors’ safety performance.
The employer shall inform contract employees of the known fire, explosion, or
toxic release hazard related to the contractor’s work and the process.
The employer shall describe applicable provisions of the emergency action
plant and control access to these process areas.
The employer must periodically evaluate the performance of contract employers
in fulfilling their obligations.
The employer will fill out a Chlorine Dioxide Work Permit with the contractors
who are working on or around the ClO2 system.
Notes: Personal safety accountability. Always look out for one another – the primary goal is to go home how we came in.

## Slide 7: Contract Employer Responsibilities
You as the contract employer are responsible for:
Ensuring that contract employees are trained in work practices necessary to do
your jobs.
Instructing employees in safe work practices, safety rules of the facility, and the
known potential fire, explosion, or toxic release hazards relating to your
respective job functions. Including and not limited to:
  SDS reviews of chlorine dioxide and other chemicals in the area.
  Lockout/Tagout
  Confined Space Entry
  Opening Process System (Line Break)
  Provision of the emergency action plan that pertains to the area you will be
  working in.
Notes: Personal safety accountability. Always look out for one another – the primary goal is to go home how we came in.

## Slide 8: Contract Employer Responsibilities
You as the contract employer are responsible for:
The contractor shall document that each employee working
onsite has received and understood the required training listed
above. These training records shall contain the identity of the
employee, the date of the training, and the means used to
verify that the employee understood the training. For example,
quiz.
Report all illnesses and injuries to your Rumford mill contact
immediately. These will require an investigation to prevent
reoccurrence and will be maintained in the safety department.
Notes: Personal safety accountability. Always look out for one another – the primary goal is to go home how we came in.